COMPARISON BETWEEN WATER DISTILLATION PROCESS AND HYDROGEN ISOTOPE EXCHANGE PROCESS FOR DEPLETION AND ENRICHMENT OF TRITIUM IN LIGHT WATER

# MASAMI SHIMIZU* and KENJI TAKESHITA**

*  Isotope Science Laboratory 1198 Issiki, Hayama, Kanagawa-ken 240-0111, Japan

** Dept. of Environmental Chemistry and Engineering, Tokyo Institute of Technology,

4259 Nagatsuda, Midori-ku, Yokohama 226-8502, Japan

ABSTRACT. The dimensions of typical tritium separation processes, water distillation process and the hydrogen-isotope exchange process with hydrophobic Pt-catalyst, were evaluated numerically for the recovery of tritium from wastewater generated by the decommissioning of Magnox reactor. Both the column diameter and the column height required for the hydrogen-isotope exchange process were much smaller than these for the water distillation process. The application of hydrogen-isotope exchange process to the treatment of the tritiated wastewater is effective for not only the reduction of process dimensions but also the depression of energy consumption.

1.  Introduction

When a 165-MWe Magnox reactor is decommissioned, a large amount of tritiated wastewater is generated by cutting the concrete and the steel structure of reactor (1). Then, the quantity of tritiated wastewater and the content of tritium in the wastewater are given as 7600 m3 and 2.2×1011 Bq, respectively (1). If tritium is recovered by operating an appropriate separation process for 5 yrs and then the operating time of separation process per year is given as 8000 h/y, the waste water flow rate, F, and the tritium concentration of the waste water, xF , are evaluated as

(1-1)

(1-2)

respectively. In this study, typical separation processes, the water distillation process and the hydrogen-isotope exchange process using Pt-catalyst, were applied for the recovery of tritium in the wastewater. The dimensions of these processes were evaluated numerically under the following same initial conditions,

- tritium concentration of T-enriched waste water : xp = 104xF = 2.44×10-9 T-atom fraction

- tritium concentration of T-depleted waste water : xD ≤ 1×10-14 T-atom fraction.

Namely, the ratio of (xP / xF) = 104 and that of (xD / xF) ≤ ( 10-14 ) / ( 2.44×10-13 ) = 0.041. When tritium concentration of the waste water xD is less than 10-14 T-atom fraction, the wastewater  is dischargeable directly to the atmosphere. When either the water distillation process or the hydrogen isotope exchange process is applied for the recovery of tritium from the wastewater, it is necessary to remove the impurities in the wastewater as a pretreatment of the wastewater. In this study, the process dimensions will be evaluated for the wastewater without impurities.

2.  Isotope Separation factors

Two isotope exchange reactions between hydrogen and tritium,

(2-1)

(2-2)

have to be considered for the numerical evaluation of proposed processes. In the previous papers (2),(3) , the isotope separation factor for Reaction (2-1), , is given as

(2-3)

and that for Reaction (2-2), , as

(2-4)

where t denotes Celsius temperature. From Eqs.(2-2) and (2-4), the separation factors of and can be calculated as the function of temperature.

3. Water distillation process

Fig.3-1 shows the schematic description of water distillation process. Tritium is enriched at the bottom of column.  The separation performance of tritium in water distillation column was described mathematically in the previous paper(4).  The ratios of tritium fraction between bottom and feed, (xP/xF) and that between top and feed, (xD/xF), are given as

(3-1)

(3-2)

respectively.

In the conditions that the process is operated at 70°C, the separation factors are calculated as

and

As shown in Eq.(1-2), the atom fraction of tritium in the feed solution is estimated as xF = 2.44x10-13. When the overall separation factor for the enrichment of tritium is given as104, the atom fraction of tritium in the production and the fraction ratio of (xD /xF) are given as xP = 2.44×10-9 and 0.041, respectively, from the mass balance equations of tritium, FxF=PxP+DxD and F=P+D.  Therefore, the molar flow rates of product water and stripped water are calculated as

The molar ratio of the production flow to the vapor flow, (P/V), is given as

where R’ denotes the reflux ratio at the top of distillation column. The molar ratio of the production flow to the depletion flow is described as

from the overall mass balance equation of tritium. From (xD /xF)=0.041 and (xP/xF)=104,

As shown in Appendix (A), the reflux ratio at the top of the distillation column, R’, has to be given as more than 23.2. Table 3-1 shows the relations among the reflux ratio (R’), the number of theoretical plates of the enriching section (M), the vapor flow rate (V) and the measure of process dimension (M·V), which were calculated from Eq.(3-1). The optimum reflux ratio, R’, and the optimum number of theoretical plates of the enriching section, M, are evaluated as 24 and 170, respectively. Then, the number of theoretical plates of the stripping section, N, is given as 111 from Eq.(3-2) substituting (’, which was calculated by the relation of (’=Ls/V = (D·R’) / [D(R’+1)].

Table3-1  The relations between the reflux ratio (R’), the number of theoretical plates of the enriching section (M), the vapor flow rate (V) and the measure of process dimension (M·V)

When a commercial packing, Sulzer Packing, was used in the distillation column, the HETP of distilltion column was reported to be 0.1m at the operating conditions that the column temperature is 70°C and the linear velocity of vapor is 1.0 m/s (op.c) (5). There- fore, the heights of the enriching section and the stripping section are evaluated as 17m and 11.1m, respectively. As shown in Appendix (B), the cross-sectional area of the distillaion column, A, is calculated as 2.06 m2 in the conditions of =233.7 mmHg and V=264 kmol/h, as shown in Ref. (5). Thus, the column diameter, Di, is given as 1.62 m.. As the latent heat of evaporation, L, is given as 1.0x104 kcal/kmol at 70°C, the energy consumption for the phase conversion between liquid and vapor, CEV, is calculated as 3062 kW from the relation of CEV= VL/860 (1kw=860 kcal/h). The operating conditions and the calculation results were summarized in Table3-2.

4.  Hydrogen isotope exchange process

4-1 Separation system

Fig.4-1  Schematic description of hydrogen-

isotope exchange process

Figures 4-1 and 4-2 show the hydrogen-isotope exchange process using Pt-catalyst, which consists of an exchange column with Pt-catalyst and an electrolyser. It should be noted that the process does not have a phase converter, H2/O2-recombiner at the top of column.  Natural water is fed to the top of the exchange column and the tritium-depleted hydrogen gas is discharged to the atmosphere. The electrolyser plays a role as a phase converter, in which H2O is decomposed electrochemically to H2 and O2. The hydrogen gas obtained is transferred to the bottom of exchange column. The exchange column has many units, which consists of a packed bed with a hydrophobic Pt catalyst and a scrubbing bed with a commercial packing, Dixon packing. The hydrophobic Pt-catalyst is a porous stylene-divinylbenzene copolymer impregnated with 0.5 wt% Pt (0.5wt% Pt/SDBC) and is 4 mm in diameter.  Tritium is transferred from H2(g) to H2O(l) in the exchange column. The overall exchange reaction of hydrogen isotope can be described as

(4-1)

The hydrogen-isotope exchange reaction between H2(g) and H2O (v),

(4-2)

takes place in the Pt-catalyst bed and that between H2O (l) and H2O (v),

(4-3)

in the scrubbing bed. Tritium is enriched at the bottom of exchange column.

4-2  Numerical calculation of hydrogen-isotope exchange process

In the n-th unit, the exchange efficiency  (c of Pt-catalyst bed and the scrubbing efficiency (b of scrubbing bed are defined as

and							                  (4-4)

respectively, where the suffix, e, denotes equilibrium.  As seen in Figs.4-1 and 4-2, the relationships among xH, yW and zW are obtained as follows,

(4-5)

where the coefficients of A to H are defined as follows,

,   	            ,            ,           ,	                ,                           ,

,                              and

Eqs.(4-5) are transformed to the following finite difference equation concerning xH.

(4-6)

where, the coeficients of p, q and r deonte as p = – ( A + DF + G ),  q = (ADF – BDF + AG + DFG + DEH ) and r = (BC – AD )(FG – EH ).  The solution of Eq.(4-6) is given as follows,

(n=0)                    		   (4-7)

where, g1, g2 and g3 denote the real roots of the following characteristic equation,

g3+pg2+qg+r=0			                          (4-8)

K1, K2 and K3 mean constants to determine the boundary conditions shown in the Section 4-3.  By Combining Eqs.(4-5) with Eq.(4-7), the atom fractions of tritium in hydrogen gas, water vapor and water are given as

(n≥1)	      		    (4-9)

(n≥0)			          (4-10)

(n≥1)	   	 (4-11)

The concentration profiles of tritium in hydrogen gas, water vapor and water of the stripping section of the multiunit hydrogen isotope exchange column are calculated by Eqs.(4-7) to (4-11). Similarly, these of the enriching section are calculated by the following equations,

(n≥0)	   	             (4-12)

(n≥1)           	                     (4-13)

(n≥0)		    	     (4-14)

(4-15)

where the bars on these symbols denote the enriching section.

4-3. Boundary conditions for calculation

The boundary conditions for the exchange column of Fig.4-1 were given as

(1)                                                                       		(4-16)

(2)  						(4-17)

(3)						(4-18)

for the enriching section and

(4)				                        	(4-19)

(5)			                        		(4-20)

(6)				                    	(4-21)

(7)                                                                 	(4-22)

(8)                                             	(4-23)

for the stripping section.  Then, the separation factor of tritium in the water electrolysis, ( El , is 5.6  at 30°C (7).  The values of , , , , and are calculated by way of the above boundary conditions and Eqs.(4-4) to (4-15).

4-4  Summery of calculation conditions and results

The calculation conditions and results were summarized in Table 4-1.   The flow rate of natural water from the top of column, NA, was assumed as a half of feed rate. Namely, the molar flow ratio, (NA/NF), was given as 0.5 instead of the minimum flow ratio, 0.183, which is required to

Table 4-1 Summery of calculation results

| Item | Calculation conditions&results | Remarks |
| --- | --- | --- |
| NF[kmol/h] | 10.56 |  |
| ZF[T atom-fraction] | 2.44(10-13 | 2.895(107 Bq/m3 water |
| NA[kmol/h] | 5.26 | Assumed as half of feed rate |
| ZA[T atom-fraction] | 2(10-17 | Concentration of tritium in natural water |
| NR[kmol/h] | 15.84 |  |
| XR[T atom-fraction] | (1(10-14 | Dischargeable directly to the atmosphere |
| Np[kmol/h] | 1.03(10-3 |  |
| Zp/ZF | 1(104 | Enrichment factor of tritium |
| P[mmHg] | 760 | Operating preasure |
| t(C | 70 | Operating temperature |
| Ug(H+V)[Nm/s] | 0.6 | (H2+vap.) gas velocity |
| (c[-] | 0.9 | Ref.(8) |
| (b[-] | 0.9 | Ref.(8) |
| Hg[m] | 0.1 | Height of catalyst bed |
| Hl[m] | 0.15 | Height of scrubbing bed |
| nE | 13.8 | No. of unit in enriching section |
| nS | 7.7 | No. of unit in stripping section |
| HE[m] | 4.14 | Height of enriching section. Height of unit is assumed as 0.3 m/unit. |
| Hs[m] | 2.31 | Height of stripping section. Height of unit is assumed as 0.3 m/unit |
| Dex[m] | 0.55 | Eq.(4-24) |
| Vcat[m3] | 0.57 | Eq.(4-25) |
| CEL[kw] | 1774 | Eq.(4-26) |

obtain the enrichment factor of 104. The column diameter (DEX), the total volume of Pt-catalyst (Vcat) and the energy consumption of electrolyser (CEL) were evaluated as

[m]              	(4-24)

[m3]                	(4-25)

[kW]             	(4-26)

5. Conclusion

Table 5-1 shows the comparison of calculation results between the hydrogen-isotope exchange process and the water distillation process. It is found that the diameter and height of hydrogen-isotope exchange process are much smaller than those of water distillation process and the energy consumption of elecrolyser is reduced to about 55% of that of still of water distillation process.  It is concluded that the hydrogen-isotope exchange process is suitable for the treatment of tritiated wastewater generated by the decommissioning of Magnox reactor.

Table 5-1. Comparison between hydrogen-isotope exchange process and water distillation process

| F or NF [kmol/h] | 10.56 | Feed flow |
| --- | --- | --- |
| XF or ZF [T atom fraction] | 2.44(10-13 | Tritium in feed |
| R’ or (A[-] | R’=LS/D=24 | (A =NA/NF=0.5 | Reflux ratio |
| D or NR [kmol/h] | D=10.559 | NR=15.839 | Depleted flow |
| xD or xR [T-atom fraction] | xD 10-14 | xR 10-14 | Release to atmosphere |
| NA [kmol/h] |  | 5.28 |  |
| zA [T-atom fraction] |  | 2 (10-17 | Tritium in Natural water |
| P or NP [kmol/h] | P=1.01( 10-3 | NP=1.03 10-3 | Production |
| xp/xF or zP/zF | 1(104 | Enrichment factor |
| (Operating conditions) |  |  |  |
| Pressure [mmHg] | 233.7 | 760 |  |
| Temperature ((C) | 70 | 70 |  |
| uV or ug(H+V) | uV=1.0 m/s (op.c) | ug(H+V)=0.6 Nm/s |  |
| (Operating constants) |  |  |  |
| HETP [m] | 0.1 |  |  |
| (c [-] |  | 0.9 | Sulzer packing (Ref.5) |
| (b [-] |  | 0.9 | Ref.8 |
| Hg [m] |  | 0.1 | Ref.8 |
| Hl [m] |  | 0.15 | Ref.8 |
| (Results of calculation) |  |  |  |
| No of theor. plates | 281 |  | M=170 N=111 |
| No of units |  | 22 | ne=14 ns=8 units |
| Height of Colum [m] | 28.1 | 6.6 | Height of unit=0.3 m |
| Diameter of Column [m] | 1.62 | 0.55 | App.(B), Eq(4-24) |
| Vcat [m3] |  | 0.57 | Eq(4-25) |
| CEV or CEL [kw] | 3062 | 1774 | App(B), Eq(4-26) |

Appendix ( A )  Reflux ratio, R’, at the top of the water distillation column

From Eq.(3-1), the following equation

(A-1 )

is obtained.  As ((1/()M+1 is positive, the numerator of Eq.(A-2 )

(A-2)

has to be positive. From the mass balance equation, (P/V) is expressed by

and (1-l) is

From these results, the limitation of reflux ratio, R’, is given as

(A-3)

Appendix ( B )	Cross-sectional area of distillation column

The cross-sectional area of distillation column can be calculated by

[m2]                     (B-1)

When uV = 1.0 m / s ( op.c )(5) for Sulzer Packing ( op.c ) ,

[m2] 	(B-2)

The column diameter calculated from Eq.(B-1) was shown in Table B-1.

Table.B-1   Evaluation of column diameter, Di, by Eq.(B-1)

| Operating pressure ( [mmHg] | 233.7 | Remarks |
| --- | --- | --- |
| Operating Temperature t [°C] | 70 |  |
| Vapor flow rate V[kmol/h] | 264 |  |
| Vapor superficial velocity uV[m/s(op.c)] | 1.0 | Reference (4) |
| Sectional area A[m2] | 2.06 | Eq (B-1) |
| Diameter of column | 1.62 |  |

# Symbols

P : T-enriched water flow rate [ kmol / h ]

V : Vapor flow rate [ kmol / h ]

(: flow ratio = Le / V

(’:flow ratio = Ls / V

Le, Ls : Flow rates of water in the enriching section and stripping one [kmol /h]

M, N :  Numbers of theoretical plate in enriching section and stripping one [-]

and : T-atom fractions of hydrogen and water vapor leaving the nth catalytic bed and those of water vapor and liquid leaving the nth scrubbing bed respectively  [-]

(H, (V and (W : Hydrogen, water vapor and water liquid flow rate [kmol / m2h]

## REFERENCES

- Proposal of Fuji Electric Co.Ltd (1997)

- J.F.Black : J.Chem.Phys , 11 , 395 ( 1943 )

- M.M.Popov : Atom Energ. SSSR , 8 , 420 ( 1960 )

- M.Shimizu and S.Hibino : Some Analyses on the Operation of Water Distillation Column , Nippon Genshiryoku Gakkaishi ( Japanese ) 4 , 313 ( 1962 )

- M.Asahara : Hydrogen Isotope Separation by Water Distillation , “Separation of Deuterium and Tritium “ ed.by Nakane , Isomura and Shimizu ( in Japanese ) , Gakujyutsu – Shuppan Centre ( Japan ) , 1982.

- M.Shimizu , T.Doi , A.Kitamoto , and Y. Takashima : Numerical Analysis on Heavy Water Separation Characteristics for a pair of Dual Temperature Multistage-Type H2/H2O-Exchange Columns , J. of Nucl. Sci. Technol. 17 , 448 ( 1980 )

- K.Takeshita, Y.Wei, M.Shimizu, M.Kumagai and Y.Takashima: Application of H2/HTO-Isotopic Exchange Method to Recovery of Tritium from Waste Water generated in Spent Nuclear Fuel Reprocessing Plant , Fusion Technol. 28 , 1572 ( 1995 )

- Private communications on the design data and the operating performance of the IPCR-PNC type tritiated D2O upgrader in the Fugen site.

# Text boxes

Fig.4-2  Schematic description of

exchange column

| R’[-] | 24 | 25 | 26 |
| --- | --- | --- | --- |
| M[-] | 170 | 169 | 168 |
| V[kmol/h] | 264 | 275 | 285 |
| M·V[kmol/h] | 4.49x104 | 4.65x104 | 4.79x104 |

Table 3-2  Summary of water distillation process

| Operating temperature | 70 | Remarks |
| --- | --- | --- |
| Vapor pressure | 233.7 mm Hg |  |
| (H/T | 1.062 |  |
| No. of theor. Plates M N (M+N) | 170 111 281 |  |
| H=(0.1)(M+N) [m] | 28.1 | HETP=0.1 m(4) |
| u [m/s (op.c)] F [kmol/h] V/F V [kmol/h] A [m2] Di [m] CEV[kw] | 1.0 10.56 25.0 264 2.06 1.62 3062 | Appendix(B) Appendix(B) Appendix(B) |