MASS AND HEAT TRANSFER ON B7 STRUCTURED PACKING AT SEPARATION OF HYDROGEN ISOTOPES BY DISTILLATION

CORNELIA CROITORU, FLOAREA POP, GHEORGHE TITESCU, IOAN STEFANESCU and MARIUS PECULEA*

National Institute of Research-Development for Cryogenic and Isotopic Technologies ICSI

RM. VALCEA, Str. Uzinei nr. 4, Tel. 0040-050-732744, Fax 0040-050-732746, Romania

*Technical University of Civil Engineering of Bucharest, Bd. Lacul Tei, nr. 124, Sector 2,

Tel. 0040-1-2421208, Fax 0040-1-2420781, Romania

1. INTRODUCTION

The paper presents theoretical and experimental data about mass and heat transfer on B7 type structured packing, in the deuterium separation by distillation. The first part of the paper is reserved to the mass transfer study in the isotopic distillation of hydrogen, and the second part is reserved to the mass and heat transfer in the case of water isotopic distillation.

- MASS TRANSFER STUDIES

2.1 Multi-tubular column model

The height of the transfer unit, efficiency measure of the liquid-vapour contact element, is based on the two film theory. It is assumed that at liquid-vapour interface, equilibrium is snapshot established and the resistance to the mass transfer in liquid and vapour bulk is negligible, all the resistance to the transfer being concentrated in vapour and liquid boundary-layers.

At the packed distillation columns the liquid flow is pellicular. If the void space of packing  is divided in N parallel tubes with dt diameter and height equal with the packed bed height (Z), one obtains a multi-tubular column. Each tube simulates the distillation in a wetted-wall column. The calculus relationship for HTU in wetted-wall column is the following [1,2,3]:

(1)

where the characteristic parameter for the structured packing is dech. The over-all mass-transfer coefficient is reported to the vapour phase, because this phase opposes the greatest resistance. KOV is calculated by the individual coefficients and slope of the equilibrium curve:

(2)

The mass transfer coefficient in vapour phase was calculated with Johnstone and Pigford relation (3), and in liquid phase with V.G. Levici correlation for Sherwood number, relations (4).

(3)

(4)

2.2 The multi-tubular column model verification

Verification of the multi-tubular column model with experimental data was done. Figure 1 presents schematiclly an experimental plant for hydrogen isotopes separation by cryogenic distillation. The distillation column for H2-HD mixture, with inner diameter of 27 mm, is equipped on a height of 550 mm with B7 type structured packing. Experimental data are shown in table 1 and figure 2. For (NTU)y calculation the Colburn formula was used [4]:

Table 1.

Experimental data

| QF (W) | Pcol (bar) | Tcol (K) | Pcond (bar) | Tcond (K) | wf (cm/s) | y1 (ppm) | y2 (ppm) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 4.6 | 3.01 | 24.7 | 2.88 | 22.7 | 0.53 | 88 | 703 |
| 4.6 | 3.01 | 24.7 | 2.91 | 24.53 | 0.53 | 93.7 | 759 |
| 10.2 | 3.07 | 24.79 | 2.95 | 24.6 | 1.13 | 89.5 | 742 |
| 10.4 | 2.82 | 24.4 | 2.72 | 24.24 | 1.22 | 82 | 696 |
| 14.82 | 3.02 | 24.71 | 2.86 | 24.46 | 1.7 | 126.2 | 713 |
| 14.82 | 3.01 | 24.7 | 2.86 | 24.46 | 1.71 | 119 | 718 |
| 15.6 | 2.98 | 24.65 | 2.8 | 24.37 | 1.82 | 88.6 | 550 |
| 16 | 3 | 24.68 | 2.8 | 24.37 | 1.85 | 84 | 563 |
| 20.15 | 3 | 24.68 | 2.85 | 24.4 | 2.33 | 131 | 723 |
| 20.15 | 3 | 24.68 | 2.85 | 24.45 | 2.33 | 115.5 | 733.6 |
| 20.7 | 3 | 24.68 | 2.8 | 24.37 | 2.39 | 89.9 | 539 |
| 20.15 | 2.78 | 24.33 | 2.6 | 24.04 | 2.48 | 70.9 | 558.2 |
| 23.52 | 2.98 | 24.65 | 2.78 | 24.33 | 2.74 | 133 | 563.5 |
| 24.99 | 3.04 | 24.74 | 2.85 | 24.45 | 2.86 | 150 | 708.5 |
| 24.99 | 2.98 | 24.65 | 2.81 | 24.38 | 2.91 | 168 | 740.7 |
| 24.99 | 2.96 | 24.62 | 2.8 | 24.37 | 2.93 | 152 | 718.5 |
| 29.25 | 3 | 24.68 | 2.8 | 24.37 | 3.38 | 160 | 710.8 |
| 33.28 | 2.97 | 24.63 | 1.69 | 22.25 | 3.88 | 56 | 508.9 |
| 33.63 | 3 | 24.68 | 2.78 | 24.33 | 3.89 | 117 | 670.8 |

In the case of hydrogen distillation, the theoretical values of the height of the transfer unit, calculated by means of equivalent diameter of packing, are closed to those experimentally determined.

Figure 1. Schematic diagram of the experimental cryogenic plant

3. MASS AND HEAT TRANSFER STUDIES

3.1. Mathematical model

A more complex study, for the mass and heat transfer, was performed on water isotopic distillation, also considering the packing bed a multi-tubular wetted-wall column [5]. The steady-state mathematical model for the mass and heat transfer includes the following equations: overall mass balance, isotopic balance over the liquid or vapour volume element, the mass transfer between vapour and liquid phases, the heat balance over the liquid or vapour volume element, the heat transfer between vapour and liquid phases

(6)

(7)

(8)

The mathematical model has been completed with relations for the estimation of the mass and heat transfer coeficients.

3.2. Experimental data

The experimental plant for water distillation is represented schematically in figure 3. The distillation column has an inner diameter of 108 mm and it is equipped with B7 type structured packing on 14 m height. The column has 12 points for temperature and concentration measurement, which allowed us to determine the locale values of the mass and heat transfer coefficients, presented in figure 4 and 5. It can be noticed, at the column top, the influence of subcooled reflux and between stratum 4 and stratum 5 imperfections of the column insulation.

In water distillation the values of the height of the mass transfer unit range within 50-150 mm domain. Between the theoretical estimation of a distillation column functioning and the measured values one can observe a relative error ranging within 8 - 19% domaine. This fact requires correction, by means of the experimental data, for the coefficients used in the criterion relations.

4. Conclusions

The HTU mean value at water distillation (~0.1 m) is closed of the HTU mean value at hydrogen distillation (~0.2 m).

The HTU values, experimentally or theoretically obtained, constitute designing data for the hydrogen and heavy water plants. Determined values of HTU for the H2 - HD and H2O – HDO – D2O isotopic mixture distillation enter thus in practice.

The level of the mass and heat transfer coefficient, evaluated theoretically and verified experimentally, are comparable with other separation processes from the chemical industry. This fact justifies the use of the multi-tubular wetted-wall model for the description of the transfer processes in distillation columns equipped with B7 ordered packing.

BIBLIOGRAPHY

1. Floarea Pop, Marius Peculea and Cornelia Croitoru - Experimental Determination of the Height of Transfer Unit at the Hydrogen Isotopic Distillation on Ordered Packing, B7 Type", Revue Roumaine de Chimie, nr. 2, 1999

2. A. Paris - "Les procédés de rectification dans l'industrie chimique", Dunod - Paris, 1959

3. T. Yamanishi, K. Okuno, Y. Naruse, E. Sada - "Analysis of Characteristics of Cryogenic Distillation Column in Separation of Hydrogen Isotopes", Journal of Chemical Engineering of Japan, vol. 26 nr. 1 (1993)

4. E. P. Dutkai - "Coloane cu umplutură în tehnologia chimică", Editura Tehnică Bucuresti, 1977

5. C. Croitoru, F. Pop, Gh. Tiţescu, M. Culcer, M. Iliescu ş.a. - Experimentari asupra transferului de masa si caldura în coloane echipate cu umplutura ordonata tip B7, raport de cercetare, C43/14.06.2001, ICSI Rm. Valcea

Symbols

(HTU)y – height of transfer unit reported to vapour phase

L, L’, V, V’ – liquid, vapour flow rate

dech – equivalent diameter

Dc – column diameter

 - voidage of packing

K’y, K’t; kL, kV - global mass and heat transfer coefficient; liquid, vapour partial film mass heat transfer coefficient

m - slope of equilibrium curve

P - total pressure

m, V - molar liquid density, vapour density

- thickness of mass transfer boundary layer of liquid phase

A, Al, Av, al-v – area of free column section, liquid , vapour flow section area , interfacial area

DL, DV – Diffusion coeficient

Sh, Re, Sc - Sherwood, Reynolds, Schmidt number

z -height

x, y - liquid, vapour phase isotopic concentration

cp - heat capacity

tL, tV - liquid, vapour temperature

# Text boxes

Figure 2. HTU variation with the vapour velocity

P = 3 bar

experimental date

calculated date

C1, C2 – condensers

CD – distillation column

B -  boiler

Figure 3. Schematic diagram of the experimental water distillation plant