AN ACCURATE CONTROL OF THE REACTION ZONE IN THE PRODUCT REFLUXER OF 15N SEPARATION PLANT

M.Kaucsár,  V.Cosma,  D.Axente,  A.Bâldea,  Şt.Popescu,  I.Dobocan,  D.Zotoiu

National Institute for Research and Development of Isotopic and Molecular Technologies

71-103 Donath Str., P.O.Box 700, RO-400293 Cluj-Napoca 5, Romania

In order to assure the conditions for the 15N/14N isotopic exchange in NO, NO2 – HNO3 system on (packed) separation columns, one of the most important task is to maintain the same position of the chemical reaction zone between HNO3 (s) and SO2 (g) on the packing in the product refluxers [1] , [2]:

2HNO3 + 3SO2 + 2H2O  (  2NO + 3H2SO4

2HNO3 + SO2  (  2NO2 + H2SO4

The flow-rates of the nitric acid solution in the separation columns are maintained using metering pumps. The position of the reaction zone in the product refluxers was kept at an optimal height controlling the flow of the sulphur dioxide by means of a fuzzy logic controller [3].

The first action of the control procedure is the accurate localization of the chemical reaction zone in the product refluxers by sampling the temperature along the refluxer, with seven special temperature sensors. The temperature distribution in the refluxer is computed by spline interpolation.

Cubic spline interpolation is a useful computing technique to interpolate between known sampled points, due to its smooth characteristics [4] - [6]. Unfortunately it does not prevent overshoot at intermediate points, which is essential for many chemical engineering applications. The developed interpolation method prevents overshooting by reducing of smoothness. It combines the smooth curve characteristics of spline interpolation with the non-overshooting behaviour of linear interpolation [7]. That was achieved by eliminating the requirement for equal second order derivatives at every point and replacing it with specified first order derivatives. The position and the maximum value are accurately obtained by computing the first derivative, the developed algorithm being fast enough to run in real time.

Bibliography:

- Benedict, M., Pigford, T.H., Levy, H.W.  –  Nuclear Chemical Engineering, McGraw-Hill Book Co., Boston, 1998.

- Kaucsár M.,  Cosma, V.,  Axente, D.,  Bâldea, A.,  Bunea, V.  –  Fuzzy Logic Control of  15N Separation Plant.  Proceedings of the 3-rd Conference on Isotopic and Molecular Processes, Sept. 2003, Cluj-Napoca, Vol.1, pp.112-118.

- Jantzen, J.  –  Design of Fuzzy Controllers. Technical University of Denmark, Department of Automation, Denmark, Tech. report no 98-E 864, September 30, 1999.

- Van Loan, Ch.F.  –  Introduction to Scientific Computing.  1997, New Jersey, Prentice Hall

- Shene, C.-K.   –  CS3621 Introduction to Computing with Geometry Notes. Dec. 2003, Department of Computer Science, Michigan Technological University, http://www.cs.mtu.edu/%7Eshene/COURSES/cs3621/NOTES/notes.html

- Laflin, S  –  Curve Fitting - Approximation and Interpolation.  Aug. 1999, School of Computer Science, The University of Birmingham, http://www.cs.bham.ac.uk/%7Eslb/sem307/gchap8.html

- Kruger, C.J.C.  –  Constrained Cubic Spline  -  Interpolation for Chemical Engineering Applications.  Dec. 2002, Korf Software, 5 Sometons Close, Guildford, Surrey, GU2 9YB, England, http://www.korf.co.uk/spline.pdf